## Slide 1: LAB - 03
陳培殷
國立成功大學 資訊工程系

## Slide 2: Outline
Video preview for 布林代數+全及項
Mid Exam
Lab I -- Comparator
Lab II -- Constant Multiplier
Lab III(practice) -- Constant Comparator

## Slide 3: Mid Exam
考試日期 :
  10/08(四) 09:00-12:00
考試方式 : 以個人為單位
考試時間 : 50 min

## Slide 4: Three representations for a circuit
F1=x+y’z
1. Boolean Algebra
3. Circuit Diagram
2. Truth Table
Inputs
n input variables  2n combinations
真值表

## Slide 5: 74LS08
AND gate
F=xy
Boolean Algebra

## Slide 6: 74LS32
OR gate
F=x+y
Boolean Algebra

## Slide 7: 74LS04
NOT gate
F=x’
Boolean Algebra

## Slide 8: 74LS00
NAND gate
Not - AND
F=(xy)’
Boolean Algebra

## Slide 9: Top View of the Solderless Breadboard
: connected : disconected
Let a input be shared to multiple logic gate
Let a VCC be shared to multiple logic gate

## Slide 10: Example: Connection with 74LS00 Chip
Board
output
input
power supply
Wire connection & IC placement
TTL mode
Chip(NAND)

## Slide 11
There are two inputs denoted as A and B. Both A and B are 1-bit value. A comparator is designed to determine whether A is equal to B or not. The output results are represented with E .
The function and truth table of the comparator is described as follows.
Lab I – Comparator (1/2)
  E =
A | B | E
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
用全及項的概念去推導布林表示式

## Slide 12
Lab I – Comparator (2/2)
Please
  (a) write Boolean algebra of the comparator.
  (b) implement the circuit on the breadboard.

## Slide 13: Components needed for LAB I
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 14: Notice for LAB I
Input
Output
B
A
E

## Slide 15
There is a 2-bit input X (represented as X1 and X0). A constant multiplier is designed to multiply the input by 3. Finally, show the result with decimal format (0, 1, 2, …..,9) on Digital Display in the breadboard.
Hint-1:
The output digital number is 0, 3, 6 or 9, respectively, for four different inputs (0, 1, 2, 3).
Lab II -- Constant Multiplier (1/4)
MSB

## Slide 16
Lab II -- Constant Multiplier (2/4)
D | C | B | A | DIGITAL DISPLAY
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
Hint-2:
Function of the Digital Display in the breadboard is as follows.

## Slide 17
Lab II -- Constant Multiplier (3/4)
X1 | X0 | Decimal |  | D | C | B | A | Decimal
0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 1 | 1 | 3
1 | 0 | 2 |  | 0 | 1 | 1 | 0 | 6
1 | 1 | 3 |  | 1 | 0 | 0 | 1 | 9
Hint-3:
Write Boolean Algebra. (D = ? C = ? B = ? A = ?)
用全及項的概念去推導布林表示式
Notes: A+b+c+d=0
A’+B’+C+D=3

## Slide 18
Lab II -- Constant Multiplier(4/4)
Please
  (a) draw the circuit diagram of the constant multiplier.
  (b) implement the circuit on the breadboard, and show the result with decimal format (0, 1, 2, …..,9) on Digital Display in the breadboard.

## Slide 19: Components needed for LAB II
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 20
There are a 3-bit input X (represented as X2, X1 and X0) and two 1-bit outputs A and B. The comparator is designed to let output A be 1 if X>3 and output B be 1 if X>4.
The function of the comparator is described as follows.
Lab III – Constant Comparator(practice) (1/2)
  A =
  B =
MSB
LSB

## Slide 21
Lab III– Constant Comparator (practice) (2/2)
Please
  (a) draw the truth table of the comparator where three input bits are X2, X1 and X0, and two output bits are A and B, respectively.
  (b) implement the circuit on the breadboard.

## Slide 22: Components needed for LAB II
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 23: Notice for LAB III
Input
Output
X0
X1
X2
A
B