## Slide 1
陳培殷
國立成功大學 資訊工程系
數位系統實驗
Thu 9:00 am – 12:00 am

## Slide 2: Outline
Video preview for 數位系統簡介+邏輯閘+布林代數
Lab I--Boolean Algebra
Lab II--XOR
Lab III--Half Adder
Lab IV(practice)--Comparator

## Slide 3: Three representations for a circuit
F1=x+y’z
1. Boolean Algebra
3. Circuit Diagram
2. Truth Table
Inputs
n input variables  2n combinations
真值表

## Slide 4: 74LS08
AND gate
F=xy
Boolean Algebra

## Slide 5: 74LS32
OR gate
F=x+y
Boolean Algebra

## Slide 6: 74LS04
NOT gate
F=x’
Boolean Algebra

## Slide 7: 74LS00
NAND gate
Not - AND
F=(xy)’
Boolean Algebra

## Slide 8: 74LS00
Vcc (5V)
ground
A1 B1 Y1
B3 A3 Y3
NAND gate

## Slide 9: The Solderless Breadboard in CSIE NCKU
Top view of the breadboard
AND
OR
NAND
NOT

## Slide 10: Top View of the Solderless Breadboard
: connected : disconected
Let a input be shared to two logic gate

## Slide 11: Example: Connection with 74LS00 Chip(1/7)
Board
output
input
power supply
Wire connection & IC placement
TTL mode
Chip(NAND)

## Slide 12: Example: Connection with 74LS00 Chip(2/7)
Board : wire connection
ground
Vcc (5V)
Chip(NAND)

## Slide 13: Example: Connection with 74LS00 Chip(3/7)
Power supply
VCC
GND

## Slide 14: Example: Connection with 74LS00 Chip(4/7)
Signal input

## Slide 15: Example: Connection with 74LS00 Chip(5/7)
Signal output

## Slide 16: Example: Connection with 74LS00 Chip(6/7)
Input 11
Output 0
Input |  | Output
A | B | Y
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
74LS00 truth table
Y
A
B

## Slide 17: Example: Connection with 74LS00 Chip(7/7)
Input 00
Output 1
Input |  | Output
A | B | Y
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
74LS00 truth table
Y
A
B

## Slide 18: Lab I
Please draw their Truth Tables and implement the circuits with breadboard.
  F1(A, B) = (A+B’)(A’+B)
  F2(A, B) = (AB)’(A + B)
Notes: 錯誤：此時不需化簡(已修正)

## Slide 19: Components needed for LAB I
Names | Amount
Solerless Breadboard | ×1
74LS00 | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 20: Lab II – XOR (1/2)
F = A + B
1. Boolean Algebra
3. Circuit Diagram
2. Truth Table
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
F
=> F = A’B + AB’

## Slide 21: LAB II -- XOR (2/2)
Please
  (a) implement the circuit on the breadboard.

## Slide 22: Components needed for LAB II
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 23
  A half adder (HA) consists of two inputs (A and B) and two outputs (Sum and Carry). “A” denotes the summand and “B” is the addend. Sum and Carry mean the output sum and carry for input “A” and “B”. The truth table and Boolean algebra for the half adder are as follows.
LAB III -- Half Adder (1/5)
A | B | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
 |  | A
+ |  | B
 | Carry | Sum
Example:

## Slide 24: LAB III -- Half Adder (2/5)
Please
  (a) implement the circuit on the breadboard and show the result on LED.
  (b) show the result with decimal format (0, 1, 2, …..,9) on Digital Display in the breadboard.

## Slide 25
  A half adder (HA) consists of two inputs (A and B) and two outputs (Sum and Carry). “A” denotes the summand and “B” is the addend. Sum and Carry mean the output sum and carry for input “A” and “B”. The truth table and Boolean algebra for the half adder are as follows.
LAB III -- Half Adder (3/5)
A | B | Carry | Sum | Decimal
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 2
 |  | A
+ |  | B
 | Carry | Sum
Example:

## Slide 26
Digital Display in the breadboard
D | C | B(Carry) | A(Sum) | DIGITAL DISPLAY
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
Function of the Digital Display in the breadboard is as follows.

## Slide 27: Components needed for LAB III
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 28
There are two inputs denoted as A and B. Both A and B are 1-bit value. A comparator is designed to determine whether A is equal to B or not. The output results are represented with E .
The function and truth table of the comparator is described as follows.
Lab IV – Comparator (1/2)
  E =
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 29
Lab IV – Comparator (2/2)
Please
  (a) Write boolean algebra and implement the circuit on the breadboard.

## Slide 30: Components needed for LAB IV
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1